## Slide 1: AcuLive:
Acoustic Liveliness Detection
Cyan Subhra Mishra | Gulsum Gudukbay | Sethu Jose
cyan@psu.edu | gulsum@psu.edu | sethu@psu.edu
Protecting Smart Assistants from Smarter Attacks

## Slide 2: Motivation – Voice Assisted Devices
Prevalent but unsecure
Direct and Indirect attacks
  Activation by Recorded Voice of owner
  Breach by inaudible frequencies
And Many More…

## Slide 3: Motivation – Voice Assisted Devices
Protect Them from Digital Break-ins
  Voice Profile Match
  Securing from inaudible frequencies
  Two factor authentication

## Slide 4: What If Adversary Tries To Breach By Using Owners’ Recorded Voice?
AcuLive

## Slide 5: Key Challenges
Finding Pattern
Privacy
Gathering Data
Scalability
Quality
Speed
Efficiency
Cost

## Slide 6: Finding a Pattern
Actual Voice
Recorded Voice
Tested on a open voice data set, with more than 60 samples and multiple devices

## Slide 7: Understanding the FFT Pattern
Diaphragm acceleration vs Output frequency for a speaker with input frequency
Speakers are non-linear
Higher order harmonics will be observed
Unavoidable And Prominent In All Speakers: The Pattern Is Coherent And Prevalent

## Slide 8: Data Collection and Conditioning
Open Voice Data
Recording
FFT
Filter
Trim
Original (O)
Recorded (R)
2 Devices
On both O & R
Band-pass to remove inaudible
1KHz - 10KHz
Normalize

## Slide 9: Building Classifiers
Naïve Thresholding
Triangulation Thresholding
Linear Regression

## Slide 10: Naïve Thresholding
Formulation
User tunable Parameters:
Pros and Cons
Easy to Implement
User Configurable
Static Thresholding
Easily Biased By The Outliers
Does Not Adapt
Too Many False Positives

## Slide 11: Naïve Thresholding: Results
Confidence = 71.753%

## Slide 12: Naïve Thresholding: Results
Confidence = 6. 361%

## Slide 13: Triangular Thresholding
The convolution is enclosed in a right triangle between the maximum peak and the last data point
Find the x-value of the point with the greatest distance between the point and the hypotenuse of the triangle, in a line perpendicular to the hypotenuse.

## Slide 15: Triangular Thresholding: Results
We achieved a 100% accuracy with 65 sound samples.
The last 20 samples were noisy, where we played a high frequency music in the background and we still got completely accurate results.
The 100% accuracy was achieved when the threshold for the differences between recorded and actual voice signal tail portion sums was 0.18.
  This value also avoids false positives.
For larger thresholds, the accuracy decreased significantly and there were false positives.
Sum Differences Threshold | Accuracy %
0.18 | 100.00
0.30 | 98.46
0.40 | 83.08
0.50 | 64.62
0.60 | 58.46

## Slide 16: Linear Regression: Formulation
Trained Model
Trained Model
𝐹(𝑅, 𝑂)
Moments
𝑦_𝜇=𝑚_𝜇∗ 𝜇_𝑡+𝑐_𝜇 𝑦_𝜎=𝑚_𝜎∗ 𝜇_𝜎+𝑐_𝜎
𝐶=𝑓(𝑦_𝜇,𝑦_𝜎)
𝐶𝑙𝑎𝑠𝑠= {█(𝑅𝑒𝑐;𝑖𝑓 𝐶>𝑡ℎ𝑟𝑒𝑠 @𝐴𝑐𝑡;𝑖𝑓 𝐶<𝑡ℎ𝑟𝑒𝑠)┤
Average
Average (𝜇_𝑡)
Variance
Variance 〖(𝜎〗_𝑡)

## Slide 17: Linear Regression: Parameters
Regression on Mean
Best-fit values
Slope: 5.425 ± 0.8111
Y-intercept: 0.1050 ± 0.07025
95% Confidence Intervals
Slope: 3.835 to 7.015
Y-intercept: -0.03266 to 0.2427
Equation
Y = 5.425*X + 0.1050
Regression on Variance
Best-fit values
Slope 2.923 ± 1.258
Y-intercept 0.2674 ± 0.1091
95% Confidence Intervals
Slope 0.4561 to 5.389
Y-intercept 0.05352 to 0.4813
Equation
Y = 2.923*X + 0.2674

## Slide 18: Linear Regression: Results
26 | 81.162 | 64.813 | Recorded | True Positive
59 | 40.380 | 42.839 | Not Recorded | False negative
35 | 81.240 | 64.855 | Recorded | True Positive
41 | 87.369 | 68.157 | Recorded | True Positive
07 | 62.646 | 54.836 | Recorded | True Positive
23 | 56.872 | 51.725 | Recorded | True Positive
02 | 21.046 | 32.422 | Actual | True Negative
26 | 81.162 | 64.813 | Recorded | True Positive
59 | 40.380 | 42.839 | Not Recorded | False negative
35 | 81.240 | 64.855 | Recorded | True Positive
41 | 87.369 | 68.157 | Recorded | True Positive
07 | 62.646 | 54.836 | Recorded | True Positive
23 | 56.872 | 51.725 | Recorded | True Positive
02 | 21.046 | 32.422 | Actual | True Negative
# Test Data | True Positive | True Negative | False Positive | False Negative
50 of 65 | 96% | 94% | 6% | 4%

## Slide 19: Evaluation
Runtime Comparison
Naïve Thresholding | Triangular Thresholding | Regression
Naïve Thresholding | Triangular Thresholding | Regression
Evaluation Platform
Evaluated with
  Octave
  Python (TensorFlow for Regression)
Potential Deploy Platform
  Google Home
  Alexa
  Smart Watches
  Mobile Phones
Addressing Privacy
Whole processing can happen onboard
Average execution time for triangular thresholding: 1.27 sec.

## Slide 20: Key Questions and Contributions
Is this pattern prevalent?
  Yes – Tested on a open audio dataset, and different recording devices
Do we need to analyze the entire audio spectrum?
  No – Human acoustic range: 80Hz to 180Hz (Male), 165Hz to 255Hz (Female)
Do we need to add extra hardware?
  No – AcuLive builds on the existing infrastructure (including smartwatches)
What are the performance and power tradeoffs?
  Proposed algorithm is linear time, adaptive
Privacy?
  Simpler algorithm – runs on the device, NO cloud connection needed

## Slide 21: Application Domain
AcuLive combined with the available techniques can protect from
Stealthy Attack
  For inaudible sounds
Biometric Override Attack
  Previously Recorded Sounds
Acoustic Injection Attack
  Loud noises to corrupt the sensor data

## Slide 22: Conclusion and Future Work
AcuLive uses frequency profile – can help us in detecting recorded voice
Easy to deploy and needs no further hardware and highly scalable
Aculive uses the base property of a speaker – so not so easy to fool it
But needs further improvement
  We can make it adaptive (beyond regression)
    Instead of linear classifier, we can use non-linear classifier
  Understand and test with advanced audio devices
  Hardware to detect vocal chord vibration – can further strengthen
  Stealthy attack handling for inaudible sound signals and shadow frequencies.
  Energy requirements should be investigated

## Slide 23: Resources
Nirupam Roy, Haitham Hassanieh, and Romit Roy Choudhury. 2017. Backdoor: Making microphones hear inaudible sounds. In Proceedings of the 15th Annual International Conference on Mobile Systems, Applications, and Services. ACM, 2–14.
G.W. Zack, W.E. Rogers, S.A. Latt, Automatic measurement of sister chromatid exchange frequency, J. Histochem. Cytochem. 25 (7) (1977) 741-753.

## Slide 24: Thank You 